## Slide 1: Principles of Robot Autonomy I
Image processing, feature detection, and feature description

## Slide 2: Attendance Form

## Slide 3: What I would improve if I had to give the lecture again
1st it was not clear for students to go from an image to a signal (add some graphic as above) The descriptors were unclear, especially regarding how they are generated visually. Consider providing a step-by-step visual explanation of descriptor generation.
Conduct an in-class exercise to demonstrate that the descriptor operation is associative.
The slight gradient for the Marco descriptor in high-resolution images was not visible at all. At to slides an example on how to apply a filter to an image and move it around – go from 1D to 2D may be very natural to understand.
My explanation of the properties of feature descriptors was not systematic, which may have caused confusion.
Visualizations on static images often confused students, particularly concepts like scale invariance, as the connection between the visual and the underlying principle was not fully clear.

## Slide 4: From 3D world to 2D images
So far we have focused on mapping 3D objects onto 2D images and on leveraging such mapping for calibration / scene reconstruction
Next step: how to represent images and infer visual content?

## Slide 5: Visual Inertial Odometry
Campos, Carlos, Richard Elvira, Juan J. Gómez Rodríguez, José MM Montiel, and Juan D. Tardós. "Orb-slam3: An accurate open-source library for visual, visual–inertial, and multimap slam." IEEE transactions on robotics 37, no. 6 (2021): 1874-1890.

## Slide 6: Motivation: Visual Inertial Odometry
Campos, Carlos, Richard Elvira, Juan J. Gómez Rodríguez, José MM Montiel, and Juan D. Tardós. "Orb-slam3: An accurate open-source library for visual, visual–inertial, and multimap slam." IEEE transactions on robotics 37, no. 6 (2021): 1874-1890.

## Slide 7: From 3D world to 2D images
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.

## Slide 8: From 2D images to a 3D world
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.

## Slide 9: From 2D images to a 3D world
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.

## Slide 10: From 2D images to a 3D world
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.
Ideas on improving the reconstruction ?

## Slide 11: Lets and another image
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.
Any other ideas ?

## Slide 12: Confidence Threshold
Wang, Jianyuan, Minghao Chen, Nikita Karaev, Andrea Vedaldi, Christian Rupprecht, and David Novotny. "Vggt: Visual geometry grounded transformer." In Proceedings of the Computer Vision and Pattern Recognition Conference, pp. 5294-5306. 2025.

## Slide 13: Agenda
Agenda
  Fundamental tools in image processing for filtering and detecting similarities
  Basic methods to detect and describe key features in images
Readings:
  Chapter 9, sections 9.1 – 9.3 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 14: How to represent images?

## Slide 15: Image processing pipeline
Signal treatment / filtering
Feature detection (e.g., DoG)
Feature description (e.g., SIFT)
Higher-level processing

## Slide 16: Image filtering
Filtering: process of accepting / rejecting certain frequency components
Starting point is to view images as functions , where represents intensity at position
A color image would give rise to a vector function with 3 components
Represented as a matrix
i
j

## Slide 17: Spatial filters
A spatial filter consists of
  A neighborhood of pixels around the point under examination
  A predefined operation F that is performed on the image pixels within

## Slide 18: Linear spatial filters
Filters can be linear or non-linear
We will focus on linear spatial filters
Filter F (of size ) is usually called a mask, kernel, or window
Dealing with boundaries: e.g., pad, crop, extend, or wrap
Filtered image
Original image
Filter mask

## Slide 19: Linear spatial filters
Filtered image
Original image
Filter mask

## Slide 20: Linear spatial filters
Filtered image
Original image
Filter mask

## Slide 21: Linear spatial filters
Filtered image
Original image
Filter mask

## Slide 22: Image filtering
Filtering: process of accepting / rejecting certain frequency components
Starting point is to view images as functions , where represents intensity at position
A color image would give rise to a vector function with 3 components
Represented as a matrix
i
j

## Slide 23: Filter example #1: moving average
The moving average filter returns the average of the pixels in the mask
Achieves a smoothing effect (removes sharp features)
E.g., for a normalized mask
Generated with a 5x5 mask
What happens with the edges ?

## Slide 24: Filter example #2: Gaussian smoothing
Gaussian function
To obtain the mask, sample the function about its center
E.g., for a normalized mask with

## Slide 25: Convolution
Still a linear filter, defined as
Same as correlation, but with negative signs for the filter indices
Correlation and convolution are identical when the filter is symmetric
Convolution enjoys the associativity property
Example: smooth image & take derivative = convolve derivative filter with Gaussian filter & convolve the resulting filter with the image

## Slide 26: Convolution

## Slide 27: Convolution

## Slide 28: Convolution
Associativity

## Slide 29: Differentiation Intuition
What is differentiation in the context of images ?

## Slide 30: Differentiation Intuition

## Slide 31: Differentiation Intuition
What filter size do we need?
What are the values ?

## Slide 32: Differentiation
Derivative of discrete function (centered difference)
Derivative as a convolution operation; e.g., Sobel masks:
Note: masks are mirrored
In convolution
Along x direction
Along y direction

## Slide 33: Similarity measures
Filtering can also be used to determine similarity across images (e.g., to detect correspondences)
Sum of absolute differences
Sum of squared differences

## Slide 34: Detectors
Goal: detect local features, i.e., image patterns that differ from immediate neighborhood in terms of intensity, color, or texture
We will focus on
  Edge detectors
  Corner detectors

## Slide 35: Use of detectors/descriptors: examples
Estimating homographic transformations
Panorama stitching
Object detection
Stereo reconstruction

## Slide 36: Edge detectors
Edge: region in an image where there is a significant change in intensity values along one direction, and negligible change along the orthogonal direction
In 1D
In 2D
Magnitude of 1st order derivative is large,
2nd order derivative is equal to zero

## Slide 37: Criteria for “good” edge detection
Accuracy: minimize false positives and negatives
Localization: edges must be detected as close as possible to the true edges
Single response: detect one edge per real edge in the image

## Slide 38: Strategy to design an edge detector
Two steps:
  Smoothing: smooth the image to reduce noise prior to differentiation (step 2)
  Differentiation: take derivatives along x and y directions to find locations with high gradients

## Slide 39: 1D case: differentiation without smoothing

## Slide 40: 1D case: differentiation with smoothing
Edges occur at maxima or minima of

## Slide 41: A better implementation
Convolution theorem:

## Slide 42: Edge detection in 2D
Find the gradient of smoothed image in both directions
Compute the magnitude and discard pixels below a certain threshold
  Non-maximum suppression: identify local maxima of

## Slide 43: Derivative of Gaussian filter

## Slide 44: Canny edge detector
Suppression

## Slide 45: Corner detectors
Key criteria for “good” corner detectors
Repeatability: same feature can be found in multiple images despite geometric and photometric transformations
Distinctiveness: information carried by the patch surrounding the feature should be as distinctive as possible

## Slide 46: Repeatability
Without repeatability, matching is impossible

## Slide 47: Distinctiveness
Without distinctiveness, it is not possible to establish reliable correspondences; distinctiveness is key for having a useful descriptor

## Slide 48: Finding corners
Corner: intersection of two or more edges
Geometric intuition for corner detection: explore how intensity changes as we shift a window
Flat: no changes in
any direction
Edge: no change along
the edge direction
Corner: changes in
all directions

## Slide 49: Harris detector: example

## Slide 50: Properties of Harris detectors
Widely used
Detection is invariant to
  Rotation -> geometric invariance
  Linear intensity changes -> photometric invariance
Detection is not invariant to
  Scale changes
  Geometric affine changes
Corner
All points classified as edges!

## Slide 51: Properties of Harris detectors
Widely used
Detection is invariant to
  Rotation -> geometric invariance
  Linear intensity changes -> photometric invariance
Detection is not invariant to
  Scale changes
  Geometric affine changes
Corner
All points classified as edges!
Scale-invariant detection, such as
Harris-Laplacian
in SIFT (specifically, Difference of Gaussians (DoG))

## Slide 52: Descriptors
Goal: describe keypoints so that we can compare them across images or use them for object detection or matching
Desired properties:
  Invariance with respect to pose, scale, illumination, etc.
  Distinctiveness

## Slide 53: Simplest descriptor
Naïve descriptor: associate with a given keypoint an window of pixel intensities centered at that keypoint
Window can be normalized to make it invariant to illumination
Main drawbacks
Sensitive to pose
Sensitive to scale
Poorly distinctive

## Slide 54: Popular detectors / descriptors
SIFT (Scale-Invariant Feature Transformation)
  Invariant to rotation and scale, but computationally demanding
  SIFT descriptor is a -dimensional vector!
SURF
FAST
BRIEF
ORB
BRISK
LIFT

## Slide 55: A different paradigm: using CNNs to detect and describe features

## Slide 56: Next time