## Slide 1: Principles of Robot Autonomy I
Information extraction

## Slide 2: Agenda
Agenda
  Introducing SiFT
  Extracting information from sensor measurements
Readings:
  Chapters 11 in PoRA lecture notes

## Slide 3: Last lecture: Recap
Image processing, feature detection and description, such as:
  Correlation / convolution filtering operations (left figure)
  Feature descriptors for detecting salient keypoints (right figure)
Canny edge detector (filter + convolution)
Keypoints from e.g., SIFT

## Slide 4: Recap Feature Detection
Repeatability: same feature can be found in multiple images despite geometric and photometric transformations
Distinctiveness: information carried by the patch surrounding the feature should be as distinctive as possible

## Slide 5: Introducing SiFT Detector
https://www.youtube.com/watch?v=4AvTMVD9ig0
https://docs.opencv.org/4.x/da/df5/tutorial_py_sift_intro.html

## Slide 6: Introducing SiFT Detector
https://www.youtube.com/watch?v=4AvTMVD9ig0
https://docs.opencv.org/4.x/da/df5/tutorial_py_sift_intro.html

## Slide 7: Introducing SiFT Descriptor
https://gilscvblog.com/2013/08/18/a-short-introduction-to-descriptors/

## Slide 8: The see-think-act cycle

## Slide 9: Information extraction
Today's focus: extracting actionable information from images
  Geometric primitives (e.g., lines and circles): useful, for example, for robot localization and mapping
  Scene understanding and object recognition: useful, for example , for localization within a topological map and for high-level reasoning
Example (Geometric primitive): Plane Fitting
Example (Scene understanding): Object detection

## Slide 10: LiDAR data

## Slide 11: See – Think – Act
(x,y,z)
1. Our robot sees points
2. We fit an elevation map to the data
3. We act based on the map representation

## Slide 12: Geometric information extraction
Geometric feature extraction: extract geometric primitives from sensor data (e.g., range data)
Examples: line, circles, corners, planes, etc.
We focus on line extraction from range data (a quite common task); other geometric feature extraction tasks are conceptually analogous
The two main problems of line extraction from range data
  Which points belong to which line?  segmentation
  Given an association of points to a line, how to estimate line parameters?  fitting

## Slide 13: Intuition Line Fitting

## Slide 14: Step #2: line fitting
It is useful to work in polar coordinates:
Equation of a line in polar coordinates
  Let be an arbitrary point on the line
  Since determine a right triangle
are the parameters of the line
Goal: fit a line to a set of sensor measurements

## Slide 15: Step #2: line fitting
Since there is measurement error, the equation of the line is only approximately satisfied
Error
Assume n ranging measurement points represented in polar coordinates as
We want to find a line that best “fits” all the measurement points

## Slide 16: Step #2: line fitting
Consider, first, that all measurements are equally uncertain
Find line parameters that minimize squared error
Unweighted least squares

## Slide 17: Step #2: line fitting
Consider, now, the case where each measurement has its own, unique uncertainty
For example, assume that the variance for each range measurement is
Associate with each measurement a weight, e.g.,
Then, one minimizes
Weighted least squares

## Slide 18: Step #2: line fitting solution
Assume that the n ranging measurements are independent
Solution:

## Slide 19: Step #1: line segmentation
Several algorithms are available
  Split-and-merge
  RANSAC
  Hough-Transform
We will focus on RANSAC

## Slide 20: RANSAC
RANSAC: Random Sample Consensus
General method to estimate parameters of a model from a set of observed data in the presence of outliers, where outliers should have no influence on the estimates of the values
Typical applications in robotics: line extraction from 2D range data, plane extraction from 3D point clouds, feature matching for structure from motion, etc.
RANSAC is iterative and non-deterministic: the probability of finding a set free of outliers increases as more iterations are used

## Slide 21: RANSAC

## Slide 22: RANSAC

## Slide 23: RANSAC

## Slide 24: RANSAC

## Slide 25: RANSAC

## Slide 26: RANSAC

## Slide 27: RANSAC

## Slide 28: RANSAC

## Slide 29: RANSAC iterations
In principle, one would need to check all possible combinations of 2 points in dataset
If , number of combinations is  too many
However, if we have a rough estimate of the percentage of inliers, we do not need to check all combinations…

## Slide 30: RANSAC iterations: statistical characterization
Let be the percentage of inliers in the dataset, i.e.,
Let be the desired probability of finding a set of points free of outliers (typically, )
Assumption: 2 points chosen for line estimation are selected independently

## Slide 31: RANSAC iterations: statistical characterization
Then minimum number of iterations to find an outlier-free set with probability at least is:
Thus if we know (at least approximately), after iterations RANSAC will find a set free of outliers with probability
Note:
  depends only on , not on !
  More advanced versions of RANSAC estimate adaptively

## Slide 32: Semantic information extraction
Semantic information: higher-level scene information in sensor data (e.g., images) like objects, their locations, and relationships
Encompasses a broad class of perception algorithms:
  Object detection, semantic segmentation, object recognition, tracking
  Conceptually: seeks to ground raw sensor data into structured information useful for downstream robot reasoning and action
Image-based semantic segmentation
LiDAR-based semantic segmentation

## Slide 33: Object detection
Example of semantic extraction: object detection
  Given a source image of an object, localize the object in the target image
  What if the object is rotated, translated, scaled, partially occluded?
  Solution: rely on stable feature detectors / descriptors for object detection
Today's detector (feature-based, still relevant!)
Modern detectors (learned-based, DNNs)

## Slide 34: Object detection
The main problems in feature-based object detection are:
  Feature matching: detect and match object features across images
  Model fitting: fit homography to predict object location in the target image
Aside on homography
  Maps plane in one image to plane in another image
  Relevant for step "b." above
Projecting bounding box using homography

## Slide 35: Step #1: Detect keypoints
Goal: Detect stable and salient keypoints of the object
Will make use of feature detectors and descriptors
  Choices include SIFT, SURF, FAST, BRISK, ORB, amongst others
  Many will work, some more efficiently or reliably depending on the setting
  In this example, we use SIFT
SIFT
Scale invariance of SIFT

## Slide 36: Step #1: Detect keypoints
Goal: Detect stable and salient keypoints of the object
Will make use of feature detectors and descriptors
  Choices include SIFT, SURF, FAST, BRISK, ORB, amongst many others
  Many will work, some more efficiently and/or reliably in a desired setting
  In this example, we use SIFT
Q: But, how do we associate keypoints in the source image to keypoints in the target image?

## Slide 37: Step #2: Match keypoints
Goal: Attempt to match keypoints across images
Matching criterion depends on choice of descriptor
  E.g., SIFT uses L2-norm, while ORB uses Hamming distance
  Threshold match scores to get an initial set of correspondences
Careful, manually set "good" match thresholds
will often produce outliers!

## Slide 38: Step #3: Model fitting and outlier rejection
Goal: Estimate homography between images and filter outliers
Another application of RANSAC: fit the model (i.e., homography) while simultaneously rejecting outlier matches
Given hypothesis homography (H), a keypoint match
is considered an "inlier" if
RANSAC in a nutshell:
Find best homography H with the most inliers
Reject outliers under best homography H

## Slide 39: Recap Transform

## Slide 40: Recap Transform
Affine Transform
Projective / Perspective / Homography Transform
https://scikit-image.org/docs/0.24.x/auto_examples/transform/plot_transform_types.html
Lines & Parallelism

## Slide 41: Step #4: Detect the object
Goal: Use homography (H) to localize object in target image
  Simply project object centroid and/or bounding box corners from source image to target image
  Note: Homographies are expressive but do not maintain parallelism – we may not get a bounding "box" in the target image! Other transformations (e.g., affine), are possible too

## Slide 42: Object tracking
Once objects are detected, how can we track them over time?
  Re-running object detection from scratch at each frame can be slow!
  Instead, object tracking exploits existing knowledge of the object (e.g., detected position) to track its motion over a sequence of images
  The problem is equivalent to estimating pixel velocities (optical flow)
Sparse optical flow
(tracking keypoints)
Dense optical flow
(tracking all pixels)

## Slide 43: Object tracking
Once objects are detected, how can we track them over time?
  Re-running object detection from scratch at each frame can be slow!
  Instead, object tracking exploits existing knowledge of the object (e.g., detected position) to track its motion over a sequence of images
  The problem is equivalent to estimating pixel velocities (optical flow)
Sparse optical flow
(tracking keypoints)
Dense optical flow
(tracking all pixels)

## Slide 44: Object tracking
  Intuition: pixel motion is small across frames
    Assumption: only need to search within a local region
  We can express the optical flow problem as:
  Solving the optical flow equation gives pixel velocities ,
    Many sparse and dense optical flow techniques have been developed, for example, the Lucas-Kanade method (sparse) and the Gunnar-Farneback method (dense)
(Taylor expansion step)
Optical flow equation*
source

## Slide 45: Object recognition
Object recognition: capability of naming discrete objects in the world
Why is it hard? Many reasons, including:
  Real world is made of a jumble of objects, which all occlude one another and appear in different poses
  There is a lot of variability intrinsic within each class (e.g., dogs)
In this class, we will look at two methods:
  Template matching (classic)
  Neural network methods (treated as a black box, see next lecture)

## Slide 46: Template matching
How can we find this guy?
Source: Sanja Fidler

## Slide 47: Template matching
Slide and compare!
Image I
Filter F
Source: Sanja Fidler

## Slide 48: Template matching
In practice, remember correlation:
One can equivalently write:
To ensure that perfect matching yields one, we consider normalized correlation, that is
Vector representation of filter
Vector representation of
neighborhood patch

## Slide 49: Template matching
Result:
Source: Sanja Fidler

## Slide 50: Template matching
Result:
Source: Sanja Fidler

## Slide 51: Template matching
Problem: what if the object in the image is much larger or much smaller than our template?
Solution: re-scale the image multiple times, and do correlation on every size!
This leads to the idea of image pyramids

## Slide 52: Image pyramids: scaling down
Naïve solution: keep only some rows and columns
E.g.: keep every other column to reduce image by 1/2 in width direction
Source:
Sanja Fidler

## Slide 53: Image pyramids: scaling down
Source:
Sanja Fidler
Naïve solution: keep only some rows and columns
E.g.: keep every other column to reduce image by 1/2 in width direction

## Slide 54: Image pyramids: scaling down
Solution: blur the image via Gaussian, then subsample
Intuition: remove high frequency content in the image
Source:
Sanja Fidler

## Slide 55: Image pyramids: scaling down
Solution: blur the image via Gaussian, then subsample
Intuition: remove high frequency content in the image
Source:
Sanja Fidler

## Slide 56: Image pyramids: scaling down
Solution: blur the image via Gaussian, then subsample
Intuition: remove high frequency content in the image
Source:
Sanja Fidler

## Slide 57: Image pyramids
A sequence of images created with Gaussian blurring and down-sampling is called a Gaussian pyramid
The other step is to perform up-sampling (nearest neighbor, bilinear, bicubic, etc.)

## Slide 58: However, classical methods can be brittle!
Sensitive to variations in rotation, etc.
Loss of spatial information
Lack of robustness (to partial occlusions, deformations, etc.)

## Slide 59: Using learned features
We can use convolutional neural networks (CNNs) to detect and describe features
Convolutional neural networks (CNNs): deep learning models for processing structured grid data, such as images, by using layers of convolutional operations to automatically learn hierarchical features and patterns
Solution: Use learned features!

## Slide 60: Uses in modern computer vision
Using CNNs for computer vision tasks took off ~2012 with the success of the AlexNet architecture for image classification on the ImageNet dataset
Today, learned features are used in many applications: image classification, object detection, image segmentation, object tracking, image generation etc.
Modern models also include GANs, transformers, etc.
Classification:
Goldfish
Semantic segmentation

## Slide 61: Next time