## Slide 1: Principles of Robot Autonomy I
Multi-sensor perception and sensor fusion
Daniel Watzenig

## Slide 2: Today’s lecture
Aim
  Introduce the topic of multi-sensor perception and sensor fusion
  Learn about Kalman filtering applied to sensor fusion
  Devise a sensor fusion algorithm for position estimation (low-level fusion)
  Introduce the topic of multi-object tracking
  Discuss emerging sensor fusion techniques
Readings
  F. Gustafsson. Statistical Sensor Fusion. 2010.
  C. Lundquist, Z. Sjanic, F. Gustafsson. Statistical Sensor Fusion: Exercises. 2015.
  D. Simon. Optimal State Estimation: Kalman, , and Nonlinear Approaches. 2006.

## Slide 3: Multi-sensor approach in robotics
Self-awareness (localization and positioning)
Situational awareness (detection and tracking)

## Slide 4: Single-sensor vs multi-sensor perception
Drawbacks of single-sensor perception
  Limited range and field of view
  Performance is susceptible to common environmental conditions
  Range determination is not as accurate as required
  Detection of artefacts, so-called false positives
Multi-sensor perception might compensate these, and provide:
  Increased classification accuracy of objects
  Improved state estimation accuracy
  Improved robustness for instance in adverse weather conditions
  Increased availability
  Enlarged field of view

## Slide 5: Using stationary sensors

## Slide 6: Sensor fusion taxonomies
Fusion level taxonomy
Fusion classes taxonomy
Data-related taxonomy
Architectural taxonomy

## Slide 7: Fusion level taxonomy
Fusion is typically divided into three levels of abstraction:
  Low-level fusion
  Intermediate-level fusion
  High-level fusion
They respectively fuse:
  Signals (early)
  Features and characteristics (deep)
  Decisions (late)
Truck
0.5
Truck
0.9
Truck
0.9
Car
0.9
Car
0.9
Car
0.2
Schematic depiction of fusion levels (Stüker, Heterogene Sensordatenfusion
zur robusten Objektverfolgung im automobilen Straßenverkehr, 2016)

## Slide 8: Comparison
[Source: K. Huang et al., Multi-modal Sensor Fusion for Auto Driving Perception: A Survey, CVPR, 2024, https://arxiv.org/abs/2202.02703]

## Slide 9: Fusion class taxonomy
Competitive fusion
  is used when redundant sensors measure the same quantity, in order to reduce the overall uncertainty
Complementary fusion
  is used when sensors provide a complementary information about the environment, for instance distance sensors with different ranges
Cooperative fusion
  is used when the required information can not be inferred from a single sensor (e.g. GPS localization and stereo vision)

## Slide 10: Architectural taxonomy
The centralized architecture is theoretically optimal, but scales badly with respect to communication and processing
The decentralized architecture is a collection of autonomous centralized systems, and has the same scaling issues
The distributed architecture scales better, but can lead to information loss because each sensor processes its information locally

## Slide 11: Data-related taxonomy
Inherent imperfection of the sensory data
The data-related taxonomy provides us with a checklist of underlying data issues and how to deal with them

## Slide 12: Data-related taxonomy
Sensory data makes a statement about the environment
  "The distance to the nearest car is 35.12 m”
Due to the inherent data imprecision, we have to deal with:
  Uncertainty: The distance to the nearest car is more than 20 m with 80% probability
  Vagueness: The distance to the nearest car is more than 20 m with 80% probability, and we are 90% confident in this statement
  Ambiguity
  Incompleteness
The underlying data can contain multiple imperfections at once

## Slide 13: Bayesian statistics in multi-sensor data fusion
Basic premise: all unknowns are treated as random variables and the knowledge of these quantities is summarized via a probability distribution
  This includes the observed data, any missing data, noise, unknown parameters, and models
Bayesian statistics provides
  a framework for quantifying objective and subjective uncertainties
  principled methods for model estimation and comparison and the classification of new observations
  a natural way to combine different sensor observations
  principle methods for dealing with missing information

## Slide 14: Sensor fusion – a simple example
Problem: determine the distance to n objects using measurements from two sensors
Assumptions:
  Both sensors have the same field of view
  First sensor has a higher precision than the second sensor
  Consider the simplest case (n=1)
How to fuse these measurements properly?

## Slide 15: Sensor fusion – a simple example
Sensors provide redundant measurements of the same physical quantity (distance)
To incorporate the precision information → measurements are assumed to be normally distributed random variables
Specifically, the univariate Gaussian distributions are:

## Slide 16: Sensor fusion – a simple example
Assumption from before:
  First sensor has a higher precision than the second sensor
This can be captured as:
Problem is to find
The idea is to combine the previous Gaussian distributions

## Slide 17: Sensor fusion – a simple example
Re-arranging the expression in the exponent and dividing the numerator and denominator by :
To obtain an expression of form in the numerator, it is necessary to add and subtract the square of the second term

## Slide 18: Sensor fusion – a simple example
The expression in the exponent becomes

## Slide 19: Sensor fusion – a simple example
Putting everything together leads to the final distribution which represents the fused information

## Slide 20: Sensor fusion – a simple example
Mean value and variance are
The fused value is the weighted average of the measurements
The weighting favors the sensor with higher precision
The overall uncertainty decreases

## Slide 21: Kalman filter (KF) – again
Assumption #1: linear dynamics
  i.i.d. process noise is
  Assumption #1 implies that the probabilistic generative model is Gaussian
Assumption #2: linear measurement model
  i.i.d. measurement noise is
  Assumption #2 implies that the measurement probability is Gaussian

## Slide 22: Kalman filter (KF)
Assumption #3: the initial belief is Gaussian
Key fact: These three assumptions ensure that the posterior is Gaussian for all t, i.e.,
Note:
  KF implements a belief computation for continuous states
  Gaussians are unimodal  commitment to single-hypothesis filtering

## Slide 23: Kalman filter: algorithm revisited
Project state ahead
Project covariance ahead
Compute Kalman gain
Update estimate with new measurement
Update covariance
Prediction
Correction
Uncertainty in correction
Uncertainty in prediction

## Slide 24: Kalman filter (KF) – pose estimation
Initial state
Time instant t-1
Car’s position
Optimal state estimate
time instant t
Measurement
Time instant t
Predicted state
Time instant t
Position
Time instant t
data fusion
Probability
density function

## Slide 25: Kalman filter (KF) – multi-sensor fusion
Motion model
Position observation
Corrected state
Predicted state
Kalman Filter Fusion
IMU
Lidar
GPS
IMU only
High rate
Low rate

## Slide 26: Sensor fusion example
Problem: Estimate position, velocity, and acceleration of a vehicle from noisy position and acceleration measurements
Assumptions:
  Single track model for the vehicle
  Lidar provides position measurements with low precision
  GPS provides position measurements with high precision
  IMU provides acceleration measurements
Sensor fusion is done using the Kalman filter

## Slide 27: Sensor fusion example: Motion model
State vector:
Change of the state over time is captured by the motion model
represents sampling time

## Slide 28: Sensor fusion example: Motion model
The motion model can be represented in matrix form
where is i.i.d. process noise distributed as
State vector
State transition matrix
Process noise

## Slide 29: Sensor fusion example: Measurement model
The measurement model defines a mapping from the state space to the measurement space
For this example, two possible fusion scenarios will be considered:
  1. Lidar + IMU
  2. Lidar + GPS + IMU
In the first scenario, only measurements from Lidar and IMU are available
  Assumption: Lidar provides low precision measurements (noisy data)
In the second scenario, high precision GPS measurements are also available

## Slide 30: Sensor fusion example: Measurement model
First scenario – measurement model is given by
where is i.i.d. measurement noise distributed as
Measurement vector
Measurement matrix
State vector
Measurement noise

## Slide 31: Sensor fusion example: Initialization
Choosing the initial state vector - depends on available information
  If there is a-priori knowledge – initialization is done with known values
  If there is a lack of information – initial state is chosen to be zero
  For this example the initial state vector is set to zero
Choosing the initial covariance matrix - should be defined based on the initialization error
  If the initial state is not very close to the correct state - will have large values
  If the initial state is close to the correct state - will have small values

## Slide 32: Sensor fusion example: Noise model tuning
The process noise covariance matrix - describes the confidence in the system model
  Small values indicate higher confidence – predicted values are more weighted
  Large values indicate lower confidence – measurements become dominant
The measurement noise covariance matrix - describes the confidence in the measurements
  Has a similar interpretation as
Both matrices need to be symmetric and positive definite

## Slide 33: Sensor fusion example: Position estimation

## Slide 34: Sensor fusion example: Position estimation

## Slide 35: Sensor fusion example: Position estimation
Estimate is very noisy because of the poor Lidar measurements

## Slide 36: Sensor fusion example: Velocity estimation

## Slide 37: Sensor fusion example: Velocity estimation

## Slide 38: Sensor fusion example: Acceleration estimation

## Slide 39: Sensor fusion example: Acceleration estimation

## Slide 40: Sensor fusion example: Acceleration estimation

## Slide 41: Sensor fusion example: New measurement model
In the previous scenario – the position estimate is quite noisy (because of the low precision of the Lidar measurements)
Now: position is measured with Lidar and GPS

## Slide 42: Sensor fusion example: Noise model tuning
The measurement noise covariance matrix for this scenario has an additional GPS variance

## Slide 43: Sensor fusion example: Position estimation

## Slide 44: Sensor fusion example: Position estimation
Combining Lidar and GPS data results in a more accurate estimation

## Slide 45: Sensor fusion example: Position variance

## Slide 46: Sensor fusion example: Conclusion
Problem: Vehicle state estimation using EKF
The example pointed out:
  How to create a motion model and a measurement model
  How to fuse the data from different types of sensors
  How to set the initial state vector and the initial covariance matrix
  How to chose appropriate values for process noise and measurement noise covariance matrices
  How to achieve a more accurate state estimation by adding more sensors
  How fusion of data decreases the overall estimation variance

## Slide 47: Useful trick
Augment the state vector with some auxiliary states and then apply the EKF to the augmented state space model
What can we handle?
    Colored state noise
    Colored measurement noise
    Sensor offset and drifts
    Sensor faults (sudden offset)
    Actuator fault (sudden offset)

## Slide 48: Live demo / Autoware by M. Schratter
Lidar- and GNSS-based localization
Parameter variation (noisy data, bias, drift)

## Slide 49: Multi-sensor approach in robotics
Self-awareness (localization and positioning)
Situational awareness (detection and tracking)

## Slide 50: Modeling the environment
Two types of algorithms are typically used (multiple sensors)
  Object tracking algorithms
  Occupancy grid algorithms
Goal of object tracking algorithms
  to determine the list of objects, which are currently present in the environment
  to estimate their state variables
Occupany grid approach
  we describe the environment in a form of a discrete grid with certain height and width of the cells (fixed resolution step size)
  each cell has a probability that it is occupied (or not), defined by sensor observations

## Slide 51: Tracking vs. occupancy grids

## Slide 52: Occupancy grids
    Unknown: not observed by the sensor
    Free: not occupied by any object
    Static: occupied by a non-moving object
    Dynamic: occupied by a moving object (information like velocity and heading)
Blue: unknown
Gray: free
Brown: static
Yellow: dynamic

## Slide 53: Single object tracking
Single model estimation filter (Kalman filter type)
Project state ahead
Project covariance ahead
Update estimate with new measurement
Update covariance
Prediction
Correction
Measurement noise is
Process noise is
Description of the system and the measurement models:

## Slide 54: Single object tracking
Vehicle model?
Vehicle is moving in different modes
Constant velocity (CV)
Constant acceleration (CA)
Constant turn rate (CT)

## Slide 55: Multi-object tracking
The difficulty of multi-object tracking
3. Track maintenance
4. Track maintenance due to uncertainties
2. Data association problem
1. Uncertainties in predictions and in measurements of the objects

## Slide 56: Multi-object tracking
When tracking multiple objects:
What are the ways to approach the data association problem?
What are the ways to address the track maintenance problem?
Multi-object tracking flow chart
KF, IMM filter…
Add/delete tracks
GNN, JPDA…
Rejecting unlikely observations
1-to-1, many-to-1, 1-to-many

## Slide 57: Sensor fusion using radar and vision data
Define Radar and Vision Sensors
Sensors defined / ego vehicle:
6 radar sensors:
  2 long-range radar sensors covering 20 degrees (in front and back),
  4 short-range radar sensors covering 90 degrees (two per side),
2 vision sensors:
  Front-facing camera located at front windshield,
  Rear-facing camera located at rear windshield,
sensors have some overlap and some coverage gap.

## Slide 58: Sensor fusion using radar and vision data
Create a Tracker
to track the vehicles that are close to the ego vehicle,
Note:
  initialize the motion model
  initialize the EKF that works with position and velocity
Assigning detections to tracks.
Initializing new tracks based on unassigned detections. All tracks are initialized as 'Tentative', accounting for the possibility that they resulted from a false detection.
Confirming tracks if they have more than M assigned detections in N frames.
Updating existing tracks based on assigned detections.
Coasting (predicting) existing unassigned tracks.
Deleting tracks if they have remained unassigned (coasted) for too long
What is the tracker responsible for?

## Slide 59: Sensor fusion using radar and vision data

## Slide 60: Sensor fusion using radar and vision data
Gaussian mixture phd tracker (here: MATLAB implementation)
Can handle multiple detections per object per sensor (here: 6 radars, 2 cameras)
It estimates the size and orientation of the object (along with pose and velocity)

## Slide 61: Takeaways
Multiple target tracking (MTT), multi-object tracking (MOT)
  multiple detections from multiple targets,
  use of one or more sensors,
  one or more tracks are used to estimate the states of the targets.
Note: Extended object tracking
  high-resolution radar/lidar sensors,
  can handle multiple detections per object.

## Slide 62: Emerging mathematical frameworks - outlook
How to handle the unpredictable nature of real-world environments?
Dynamic Bayesian filtering: from static to dynamic uncertainty
  Standard: sensor uncertainty are static, pre-defined probabilities.
  Dynamically adapt probability models based on sensor performance / environmental conditions.
  E.g., robot moves into a shadowy corner  system adjusts the weighting of visual vs. Lidar data.
Context-aware filtering
  Standard KFs rely on fixed noise models.
  Adaptive noise covariance matrices that evolve based on environmental conditions.
  Effect: reduction of estimation error e.g., in scenarios involving rapid environmental changes.
Hybrid architectures
  They combine classical filtering with modern machine learning.
  Use of neural networks to learn optimal filter parameters from experience, rather than manual tuning.
  Effect: reduced calibration time while improving accuracy.

## Slide 63: Sensor fusion attention mechanisms
Combines data from multiple sensors by dynamically weighting their contributions depending on context, reliability, and relevance.
Main benefits:
  Prioritize high-quality signals
  Suppress noisy or unreliable data
  Adapt to changing environments
  Improve robustness in edge cases
Examples:
  Rely more on LiDAR in low-light conditions
  Switch focus to camera when fine texture is needed
  Elevate radar signals in fog or rain

## Slide 64: How it works (conceptually)
Each sensor provides a feature representation
  e.g., RGB image features, Lidar point cloud features, radar Doppler features
The attention module computes similarity scores between sensor features (queries, keys, values).
These scores determine which sensors or modalities contribute more to the fused output.
The result is a context-dependent weighted fusion.

## Slide 65: Possible architecture
[Source: P. Shi et al., Att-BEVFusion: An Object Detection Algorithm for Camera and LiDAR Fusion Under BEV Features, World Electr. Veh. J. 2024, 15(11), 539; https://doi.org/10.3390/wevj15110539]

## Slide 66: Common problems in multi-sensor data fusion
Registration: Coordinates (both time and space) of different sensors or fusion agents must be aligned.
Bias: Even if the coordinate axis are aligned, due to the transformations, biases can result. These have to be compensated.
Correlation: Even if the sensors are independently collecting data, processed information to be fused can be correlated.
Data association: multi-target tracking problems introduce a major complexity to the fusion system.
Out-of-sequence measurements: Due to delayed communications between local agents, measurements belonging to a target whose more recent measurement has already been processed, might arrive to a fusion center.
…