## Slide 1: Principles of Robot Autonomy I
State space dynamics – definitions and modeling

## Slide 2: Attendance Form

## Slide 3: For urgent questions
aa174a-aut2526-staff@lists.stanford.edu
Please do not email Prof. Pavone or the CAs individually unless there is a specific reason!

## Slide 4: Agenda
State space dynamics
  Definitions
  Modeling (kinematic and dynamic models)
  Special case: LTI systems and linearization
Readings
  Chapter 1, sections 1.1 – 1.3 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 5: State space models
We can control a robot through the inputs to the system (e.g., motor torques, rotor thrusts, etc.)
The state of a robot is a collection of variables (e.g., position, velocity) that change over time in response to the inputs
A state space model is a mathematical description of how the state evolves over time (i.e., or ) in response to the inputs

## Slide 6: Example: double-integrator
Suppose we can control the force pushing on a cart
Newton’s second law tells us that
Let with , and . Then we can write

## Slide 7: Kinematic models
Kinematic models are mathematical models that describe the motion of a system without consideration of forces
Kinematic models typically result from geometric constraints on the motion of a system, before considering any forces
For example, the “unicycle” with generalized coordinates should not slip sideways, i.e.,
This relation induces a kinematic model, as we will see shortly

## Slide 8: Holonomic and nonholonomic constraints
More broadly, constraints on degrees of freedom come in various forms: Pfaffian constraints are a special, yet common case of nonholonomic constraints
If has rows (constraints) and columns (DOFs), then where is a basis for admissible velocities, i.e., the null space of .
Kinematic model of the constrained system

## Slide 9: Back to unicycle example
The “unicycle” with DOFs should not slip sideways, i.e.,
Physically, is the forward velocity of the wheel, and is its rotational steering velocity
Notes: All admissible velocities are therefore obtained as linear combination of 𝑔_1 (𝜉) and 𝑔_2 (𝜉)
The null space in this case is spanned by the vectors [cosθ, sinθ, 0] and [0, 0, 1] which suggests that any potential motion must be made up of a linear combination of these vectors. Intuitively this would be expected because [cos θ, sin θ, 0] is the unit vector in the direction of rolling, and [0, 0, 1] would correspond to the wheel spinning but not rolling.
The constraint is non-holonomic because it implies no loss of accessibility in the configuration space of the disk. -> simple 3-step motion

## Slide 10: Unicycle and differential drive models
unicycle
differential drive
We can alternate between these kinematic models via the one-to-one input mappings:

## Slide 11: Simple car model
References:
J.-P. Laumond. Robot motion planning and control. 1998.
S. LaValle. Planning algorithms. 2006.
Simple car model
Reeds-Shepp car
Dubins car
states:
inputs:

## Slide 12: From kinematic to dynamic models
A kinematic state space model should be interpreted only as a subsystem of a more general dynamical model
Improvements to the previous kinematic models can be made by placing integrators in front of action variables
For example, for the unicycle model, one can set the speed as the integration of an action representing acceleration, that is
states: inputs:

## Slide 13: Linear time-invariant models
In general, is nonlinear, which can make it difficult to analyze
Linear time-invariant (LTI) models take the form with constant matrices and
For with , the solution is . If , the system is stable, i.e., converges to zero over time
For with , the solution is , where is the matrix exponential
Analogously to the scalar case, if for each eigenvalue of , then the system is stable

## Slide 14: Example: PD control for a double-integrator
Let with , and . Then
Choose . Then with eigenvalues . If and , then for each eigenvalue , so the cart converges to a stand-still at
This is nice, can we use linear control tools if the system is non-linear?

## Slide 15: Linearization
slope
delta
offset
Linearization approximates a nonlinear function near by a line, i.e., linear function
The “slope” of the line is the derivative of at . The change in near is the slope multiplied by the distance from
The quality of the approximation can vary with the linearization point and distance from

## Slide 16: Linearization of non-linear state-space models
For the nonlinear system , the linearization around is Since and can be vectors, we generalize derivatives to Jacobian matrices
If is an equilibrium, i.e., we can consider an LTI approximation of the system near , with state and input
When is near , we can use tools from linear systems analysis and control on nonlinear systems -- more on this later with LQR control!

## Slide 17: Example: Inverted pendulum
The dynamics are described by . In state space form with , they are
Since is an equilibrium, the linearization here is
This is close to a double-integrator! We could try to stabilize the pendulum near the upright equilibrium

## Slide 18: Example: Inverted pendulum
We try to stabilize the pendulum near the upright equilibrium:
We will later discuss how we actually simulate this system on a computer

## Slide 19: Next time

## Slide 20: Attendance Form