## Slide 1: Principles of Robot Autonomy I
Trajectory tracking

## Slide 2: Attendance Form

## Slide 3: Agenda
Trajectory tracking
  Based on differential flatness techniques
  Based on LQR techniques
Readings
  Chapter 3, sections 3.1 – 3.3 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 4: Trajectory tracking
Back to two-step design strategy
Reference trajectory and control history (i.e., and ) are computed via open-loop techniques (e.g., differential flatness)
For reference tracking (Problem 2(v-vi) in pset 1)
  Geometric (e.g., pursuit) strategies
  Linearization (either approximate or exact) + linear structure
  Non-linear control
  Optimization-based techniques (e.g., MPC)
Tracking control law

## Slide 5: The see-think-act cycle
Closed-loop control/tracking

## Slide 6: Differential flatness (recap)
A nonlinear system is differentially flat if there exists a set of outputs such that
One can then use any interpolation scheme (e.g., piecewise polynomial (spline)) to plan the trajectory of in such a way as to satisfy the appropriate boundary conditions
The evolution of the state variables , together with the associated control inputs , can then be computed algebraically from
Notes: Flat outputs are “magic coordinates” that make the system look like a chain of integrators. Once you express the system in terms of them, trajectory planning and control become much simpler — you can design trajectories for z(𝑡), then algebraically recover all required states and inputs.
Effectively, in such magic coordinates, one simply has to control a system of type: z^(q+1) = w
This is extremely useful not only for traj planning, but also for traj tracking
As usual, we first fix ideas with one example

## Slide 7: Trajectory tracking for differentially flat systems
Example: dynamically extended unicycle model
The system is differentially flat with flat outputs , in particular

## Slide 8: Trajectory tracking for differentially flat systems
Then one can use the following virtual control law for trajectory tracking:
where are control gains
Such a law guarantees exponential convergence to zero of the Cartesian tracking error

## Slide 9: Trajectory tracking for differentially flat systems
More broadly, suppose system is differentially flat: the full state and control trajectories can be computed from flat outputs
Define:
One can then design a tracking controller by using linear control techniques; in particular, for a given reference flat output define the component-wise error
, which implies
For guaranteed convergence to zero of tracking error, one can set
,
with the gains chosen so as to enforce stability

## Slide 10: LQR-based methods
The previous approach only works for differentially flat systems
How can we control more general classes of systems?
  Nonlinear control techniques
  Linear-quadratic regulation (LQR) methods

## Slide 11: LQR-based methods
The previous approach only works for differentially flat systems
How can we control more general classes of systems?
  Nonlinear control techniques
  Linear-quadratic regulation (LQR) methods

## Slide 12: Linear-quadratic regulator (LQR)
How can we regulate (i.e., drive to the origin) the linear system with minimum control effort?
We define the optimal control problem
The optimal solution is of the form where and the matrix solves the continuous time Riccati diff. equation:
with
Note: this results holds even in the more general case (just plug and in the Riccati equation)

## Slide 13: Tracking LQR – linear case
Consider the linear system and assume we would like to track a reference trajectory
Define error variables and , which leads to the dynamical system
Define optimal control problem
Optimal solution is (same as before), which leads to control

## Slide 14: Tracking LQR – nonlinear case
Consider the non-linear system and assume we would like to track a reference trajectory
Key idea: make the system “linear” by linearizing around :
As before, we get a linear system in the error variables:
Optimal solution is which leads to control (where is again obtained from the Riccati eq.)

## Slide 15: Transferring results to discrete case
Same ideas apply for discrete-time systems, i.e.,
Key difference: control is , with , where and is iteratively obtained from the discrete-time Riccati equation:
  = with
Similarly as before:
  = and =
  have the same interpretation as before, namely tracking penalty, control effort penalty, and final tracking error penalty

## Slide 16: Next time