## Slide 1: Principles of Robot Autonomy I
Robotic sensors and introduction to computer vision

## Slide 2: Attendance Form

## Slide 3: Agenda
Agenda
  Overview of key performance characteristics for robotic sensors
  Overview of main sensors for robot autonomy, e.g. proprioceptive / exteroceptive, passive / active
  Intro to computer vision
Readings:
  Chapter 6, sections 6.1 – 6.4 in D. Gammelli, J. Lorenzetti, K. Luo, G. Zardini, M. Pavone. Principles of Robot Autonomy. 2026.

## Slide 4: Sensors for mobile robots

## Slide 5: Example: self-driving cars

## Slide 7: Classification of sensors
Proprioceptive: measure values internal to the robot
  E.g.: motor speed, robot arm joint angles, and battery voltage
Exteroceptive: acquire information from the robot’s environment
  E.g.: distance measurements and light intensity
Passive: measure ambient environmental energy entering the sensor
  Challenge: performance heavily depends on the environment
  E.g.: temperature probes and cameras
Active: emit energy into the environment and measure the reaction
  Challenge: might affect the environment
  E.g.: ultrasonic sensors and laser rangefinders

## Slide 8: Sensor performance: design specs
Dynamic range: ratio between the maximum and minimum input values (for normal sensor operation)
Resolution: minimum difference between two values that can be detected by a sensor
Linearity: whether or not the sensor’s output response depends linearly on the input
Bandwidth or frequency: speed at which a sensor provides readings (in Hertz)

## Slide 9: Sensor performance: in situ specs
Sensitivity: ratio of output change to input change
Cross-sensitivity: sensitivity to quantities that are unrelated to the target quantity
Error: difference between the sensor output m and the true value v
Accuracy: degree of conformity between the sensor’s measurement and the true value
Precision: reproducibility of the sensor results

## Slide 10: Sensor errors
Systematic errors: caused by factors that can in theory be modeled; they are deterministic
  E.g.: calibration errors
Random errors: cannot be predicted with sophisticated models; they are stochastic
  E.g.: spurious range-finding errors
Error analysis: performed via a probabilistic analysis
  Common assumption: symmetric, unimodal (and often Gaussian) distributions; convenient, but often a coarse simplification
  Error propagation characterized by the error propagation law

## Slide 11: An ecosystem of sensors
Encoders
Heading sensors
Accelerometers and IMU
Beacons
Active ranging
Cameras

## Slide 12: Encoders
Encoder: an electro-mechanical device that converts motion into a sequence of digital pulses, which can be converted to relative or absolute position measurements
  proprioceptive sensor
  can be used for robot localization
Wheel encoder
Credit: Pololu
Fundamental principle of optical encoders: use a light shining onto a photodiode through slits in a metal or glass disc
Credit: Honest Sensor

## Slide 13: Heading sensors
Used to determine robot’s orientation, it can be:
  Proprioceptive, e.g., gyroscope (heading sensor that preserves its orientation in relation to a fixed reference frame)
  Exteroceptive, e.g., compass (shows direction relative to the geographic cardinal directions)
Fusing measurements with velocity information, one can obtain a position estimate (via integration) -> dead reckoning
Fundamental principle of mechanical gyroscopes: angular momentum associated with spinning wheel keeps the axis of rotation inertially stable
Credit: SNS

## Slide 14: Accelerometer and IMU
Accelerometer: device that measures all external forces acting upon it
Mechanical accelerometer: essentially, a spring-mass-damper system
with m mass of proof mass, c damping coefficient, k spring constant; in steady state
Modern accelerometers use MEMS (cantilevered beam + proof mass); deflection measured via capacitive or piezoelectric effects

## Slide 15: Inertial Measurement Unit (IMU)
Credit: SNS
Definition: device that uses gyroscopes and accelerometers to estimate the relative position, orientation, velocity, and acceleration of a moving vehicle with respect to an inertial frame
Drift is a fundamental problem: to cancel drift, periodic references to external measurements are required

## Slide 16: Beacons
Definition: signaling devices with precisely known positions
Early examples: stars, lighthouses
Modern examples: GPS, motion capture systems

## Slide 17: Active ranging
Provide direct measurements of distance to objects in vicinity
Key elements for both localization and environment reconstruction
Main types:
  Time-of-flight active ranging sensors (e.g., ultrasonic and laser rangefinder)
  Geometric active ranging sensors (optical triangulation and structured light)
Credit: https://electrosome.com/hc-sr04-ultrasonic-sensor-pic/

## Slide 18: Time-of-flight active ranging
Fundamental principle: time-of-flight ranging makes use of the propagation of the speed of sound or of an electromagnetic wave
Travel distance is given by
where d is the distance traveled, c is the speed of the wave propagation, and t is the time of flight
Propagation speeds:
  Sound: 0.3 m/ms
  Light: 0.3 m/ns
Performance depends on several factors, e.g., uncertainties in determining the exact time of arrival and interaction with the target

## Slide 19: Geometric active ranging
Fundamental principle: use geometric properties in the measurements to establish distance readings
The sensor projects a known light pattern (e.g., point, line, or texture); the reflection is captured by a receiver and, together with known geometric values, range is estimated via triangulation
Examples:
  Optical triangulation (1D sensor)
  Structured light (2D and 3D sensor)
Credit: Matt Fisher

## Slide 20: Several other sensors are available
Classical, e.g.:
  Radar (possibly using Doppler effect to produce velocity data)
  Tactile sensors
Emerging technologies:
  Artificial skins
  Neuromorphic cameras

## Slide 21: Introduction to computer vision
Aim
  Learn about cameras and camera models
  Learn about the outputs of perception and what they might be used for
Readings
  Siegwart, Nourbakhsh, Scaramuzza. Introduction to Autonomous Mobile Robots. Section 4.2.3.
  D. A. Forsyth and J. Ponce [FP]. Computer Vision: A Modern Approach (2nd Edition). Prentice Hall, 2011. Chapter 1.
  R. Hartley and A. Zisserman [HZ]. Multiple View Geometry in Computer Vision. Academic Press, 2002. Chapter 6.1.

## Slide 22: Vision
Vision: ability to interpret the surrounding environment using light in the visible spectrum reflected by objects in the environment
Human eye: provides enormous amount of information, ~millions of bits per second
Cameras (e.g., CCD, CMOS): capture light -> convert to digital image -> process to get relevant information (from geometric to semantic)
Sky
Car
Information extraction
Interpretation

## Slide 23: Computer Vision Pipeline
Scene Representation
Digital image
(array of pixel values)
Car
Car
Car
Real-world scene
Sensing device
Relevant information

## Slide 24
Scene Representation
Digital image
(array of pixel values)
Information Extraction:
Features – e.g. edges, corners, texture, colors, etc.
3D structure
Car
Car
Car
Real-world scene
Relevant information

## Slide 25
Scene Representation
Digital image
(array of pixel values)
Interpretation:
Object detection
Object tracking
Image registration
Image segmentation
Car
Car
Car
Real-world scene
Relevant information

## Slide 26: Object Detection
Goal: Detect instances of semantic objects of a certain class
  E.g. pedestrian detection, face detection
Approaches:
  Traditional methods, e.g.:
    Scale-invariant feature transform (SIFT)
    Histogram of Oriented Gradients (HOG)
  Learning-based:
    Using region proposals
    Without region proposals: You Only Look Once (YOLO), Single Shot Detector (SSD)

## Slide 27: Object Tracking
Goal: Follow and locate a specific object across a sequence of images or video frames
Applications: Autonomous driving, surveillance, augmented reality, medical imaging, sports analysis, etc.
Approaches:
  Traditional methods, e.g. mean-shift tracking or Kalman filters
  Learning-based methods, e.g. Siamese networks or recurrent neural networks (RNNs)

## Slide 28: Image Registration
Goal: Transform different sets of data into one coordinate system
Examples:
  Data from multiple photographs (e.g. with different viewpoints)
  Data from different sensors (e.g. LIDAR and RGB camera)
Source: Mathworks
Example of LIDAR-camera registration shown in Notebook 9!

## Slide 29: Image Segmentation
Semantic segmentation:
  Label each pixel in the image with a category label
  Doesn’t differentiate instances, only cares about pixels
Instance segmentation:
  Label each pixel with its object instance
  Identifies individual objects within each category
Source:
Stanford CS 231n lecture slides

## Slide 30: Information extraction and interpretation can also be done with LIDAR data!
Point cloud
Semantic segmentation
Object detection
Tasks
Images from PointNet and OctoMap
Occupancy grid map
Features
Critical points

## Slide 31: From Scenes to Digital Images
Scene Representation
Digital image
(array of pixel values)
Car
Car
Car
Real-world scene
Sensing device
Relevant information

## Slide 32: How to capture an image of the world?
Light is reflected by the object and scattered in all directions
If we simply add a photoreceptive surface, the captured image will be extremely blurred
Photoreceptive surface

## Slide 33: Pinhole camera
Idea: add a barrier to block off most of the rays
Pinhole camera: a camera without a lens but with a tiny aperture, a pinhole
Photoreceptive surface
Aperture

## Slide 34: A long history
Very old idea (several thousands of years BC)
First clear description from Leonardo Da Vinci (1502)
Oldest known published drawing of a camera obscura by Gemma Frisius (1544)

## Slide 35: Pinhole camera
Perspective projection creates inverted images
Sometimes it is convenient to consider a virtual image associated with a plane lying in front of the pinhole
Virtual image not inverted but otherwise equivalent to the actual one
Pinhole of aperture
Focal length f
Credit: FP Chapter 1

## Slide 36: Pinhole perspective
Since P, O, and p are collinear: for some
Also, z=f, hence
Image center
Optical axis
Pinhole
Image plane
Perspective
Credit: FP Chapter 1

## Slide 37: Issues with pinhole camera
Larger aperture -> greater number of light rays that pass through the aperture -> blur
Smaller aperture -> fewer number of light rays that pass through the aperture -> darkness (+ diffraction)
Solution: add a lens to replace the aperture!

## Slide 38: Lenses
Lens: an optical element that focuses light by means of refraction

## Slide 39: Next time: camera models & calibration