## Slide 1: AA203 Optimal and Learning-based Control
Introduction to MPC, persistent feasibility

## Slide 2: Roadmap
Open-loop
Indirect methods
Direct
methods
Closed-loop
DP
HJB / HJI
MPC
Adaptive
optimal control
Model-based RL
Model-free RL
Control
Optimal and learning control
Adaptive control
Feedback control
LQR
iLQR
DDP
2
Reachability analysis
LQR

## Slide 3: Model predictive control
Introduction: basic setting and key ideas
Persistent feasibility of MPC
Further reading:
  F. Borrelli, A. Bemporad, M. Morari. Predictive Control for Linear and Hybrid Systems, 2017.
  J. B. Rawlings, D. Q. Mayne, M. M. Diehl. Model Predictive Control: Theory, Computation, and Design, 2017.

## Slide 4: Model predictive control
Model predictive control (or, more broadly, receding horizon control) entails solving finite-time optimal control problems in a receding horizon fashion

## Slide 5: Model predictive control
Model predictive control (or, more broadly, receding horizon control) entails solving finite-time optimal control problems in a receding horizon fashion

## Slide 6: Model predictive control
Key steps:
At each sampling time , solve an open-loop optimal control problem over a finite horizon
Apply optimal input signal during the following sampling interval
At the next time step solve new optimal control problem based on new measurements of the state over a shifted horizon

## Slide 7: Basic formulation
Consider the problem of regulating to the origin the discrete-time linear time-invariant system
subject to the constraints
where the sets and are polyhedra
Notes: A set in ℝ^𝑛defined by finitely many linear inequalities:
𝑃={𝑥∈ℝ^𝑛:𝐴𝑥≤𝑏}
%%%
A polyhedron (plural: polyhedra) is a three-dimensional geometric solid made up of a finite number of flat polygonal faces.
A polytope is a geometric object in any number of dimensions defined by flat “faces” of appropriate dimension:
A convex polytope is also the intersection of finitely many linear inequalities:
the set of all admissible states and inputs is described by linear inequalities, i.e., it is a convex polyhedral set.

## Slide 8: Basic formulation
Assume that a full measurement of the state is available at the current time
The finite-time optimal control problem solved at each stage is
subject to

## Slide 9: Basic formulation
Assume that a full measurement of the state is available at the current time
The finite-time optimal control problem solved at each stage is
subject to
Key MPC design choices!

## Slide 10: Basic formulation
Notation:
is the state vector at time predicted at time (via the system’s dynamics)
is the input at time computed at time
Note:

## Slide 11: Basic formulation
Let be the optimal solution, then
The optimization problem is then repeated at time , based on the new state
Define
Then the closed-loop system evolves as
Central question: characterize the behavior of closed-loop system

## Slide 12: Simplifying the notation
Note that the setup is time-invariant, hence, to simplify the notation, we can let in the finite-time optimal control problem, namely
Denote
subject to

## Slide 13: Simplifying the notation
With new notation,
the closed-loop system becomes

## Slide 14: Typical cost functions
2-norm:
+
1-norm or -norm:
+ , or
where are full column ranks
Notes: For a vector 𝑥∈ℝ^𝑛:
∥𝑥∥_1=∑128_(𝑖=1)^𝑛▒∣ 𝑥_𝑖∣
For a vector 𝑥∈ℝ^𝑛:
∥𝑥∥_∞=(max⁡ )┬(𝑖=1,…,𝑛)∣𝑥_𝑖∣

## Slide 15: Online model predictive control
repeat
measure the state at time instant
obtain by solving finite-time optimal control problem
if then ‘problem infeasible’ stop
apply the first element of to the system
wait for the new sampling time

## Slide 16: Main implementation issues
The controller may lead us into a situation where after a few steps the finite-time optimal control problem is infeasible persistent feasibility issue
Even if the feasibility problem does not occur, the generated control inputs may not lead to trajectories that converge to the origin (i.e., closed-loop system is unstable) stability issue
Key question: how do we guarantee that such a “short- sighted” strategy leads to effective long-term behavior?

## Slide 17: Analysis approaches
Analyze closed-loop behavior directly generally very difficult
Derive conditions on terminal function and terminal constraint set so that persistent feasibility and closed-loop stability are guaranteed

## Slide 18: Addressing persistent feasibility
Goal: design MPC controller so that feasibility for all future times is guaranteed
Approach: leverage tools from invariant set theory

## Slide 19: Set of feasible initial states
Set of feasible initial states
A control input can be found only if

## Slide 20: Controllable sets
For the autonomous system with constraints the one-step controllable set to set is defined as
For the system the one-step controllable set to set is defined as

## Slide 21: Control invariant sets
A set is said to be a control invariant set for the system if:
, for all
The set is said to be the maximal control invariant set for the system if it is control invariant and contains all control invariant sets contained in
For autonomous systems: a set is said to be a positive invariant set for the system if ; the maximal positive invariant set contains all other positive invariant sets.
These sets can be computed by using the MPT toolbox https://www.mpt3.org/

## Slide 22: Persistent feasibility lemma
Define “truncated” feasibility set:
Feasibility lemma: if set is a control invariant set for system:
then the MPC law is persistently feasible

## Slide 23: Persistent feasibility lemma
Proof:
Since is control invariant
Thus
One can write
Thus,

## Slide 24: Persistent feasibility lemma
Proof:
Pick some . Let be the solution to the finite-time optimization problem, and be the first control. Let
Since is clearly feasible, one has . Since , one has
hence the next optimization problem is feasible!

## Slide 25: Practical significance
For , we can set . If we choose the terminal set to be control invariant, then MPC will be persistently feasible independent of chosen control objectives and parameters
Designer can choose the parameters to affect performance (e.g., stability)
How to extend this result to ?

## Slide 26: Next time
Persistent feasibility of MPC (cont'd)
Stability of MPC