## Slide 1: AA203 Optimal and Learning-based Control
Intro to learning; System identification and adaptive control

## Slide 2: Course overview
Open-loop
Indirect methods
Direct
methods
Closed-loop
DP
HJB / HJI
MPC
Adaptive
optimal control
Model-based RL
Model-free RL
Control
Optimal and learning control
Adaptive control
Feedback control

## Slide 3: Outline
Intro to learning settings

## Slide 4: Outline
Intro to learning settings
System ID
Adaptive control
MRAC: Model Reference Adaptive Control
MIAC: Model Identification Adaptive Control

## Slide 5: Feedback control
System
Reference tracking, with uncertainty
Controller
Sensor
Σ
Reference
Control
Output
–
Measurement
+

## Slide 6: Feedback control
?
Reference tracking, with uncertainty
Controller
Sensor
Σ
Reference
Control
Output
–
Measurement
+

## Slide 7: Approaches
How do we handle uncertainty?
In many cases, when uncertainties have only a small effect, a feedback controller will adequately compensate for model error
  Example: A quadrotor compensating for mild wind gusts using PID control
We can use robust control approaches (e.g., minimax control strategies)
  Example: A Harrier VTOL aircraft near hover must remain stable despite large, unpredictable air turbulence — robust control ensures safe performance even under worst-case wind conditions
We can use observed state transitions to attempt to identify patterns and improve our control strategy
  Example: A robotic arm learning to adjust its grip based on object slip detected during previous grasp attempts

## Slide 8: What can we learn?
If we want to use measurements to improve control performance, we can either:
Use measurements to directly improve controller
  Direct adaptive control
  Imitation learning
  Model-free reinforcement learning
Use measurements to learn model, use model to improve controller
  System identification
  Indirect adaptive control
  Model-based reinforcement learning

## Slide 9: What can we learn?
If we want to use measurements to improve control performance, we can either:
Use measurements to directly improve controller
  Direct adaptive control
  Imitation learning
  Model-free reinforcement learning
Use measurements to learn model, use model to improve controller
  System identification
  Indirect adaptive control
  Model-based reinforcement learning
Today
Today
Today
Upcoming weeks
Upcoming weeks
Upcoming weeks

## Slide 10: How does learning happen?
Three possible learning settings:
  “Zero” episodes: the system identification approach, in which learning is done based on data gathered before operation
  One episode: want to learn and re-optimize our controller online  this is the standard setting for adaptive control
  Multiple episodes: interact with the environment in episodes, in which the system is reset at the start of each episode; learning and policy optimization can happen between episodes  this is the standard setting for reinforcement learning

## Slide 11: Outline
Intro to learning settings
System ID
Adaptive control
MRAC: Model Reference Adaptive Control
MIAC: Model Identification Adaptive Control

## Slide 12: System identification for learning-based control
For many problems, we don’t need to learn online
A standard control engineering pipeline is to do experiments in advance to build a data-driven model of the dynamics
Then, we can use this model for planning and control without further learning online
Relies on having an engineer in the loop for learning, designing experiments, resetting the system, etc.
Linear regression is one of the main system id tools

## Slide 13: Least squares
System model
Given data , , want to minimize mean squared error:
Rewrite as
Solution (full rank ):

## Slide 14: Example: first order model
Consider a 1D first-order system with discrete-time dynamics
Linear regression representation
  ,
Comments
  Practically, least squares can be written in recursive form for efficient updates as new observations stream in
  Least squares regression may also be considered in continuous time (minimizing an error integral)

## Slide 15: Linear regression for system id
As seen before, the solution is
Gauss-Markov theorem: is the best linear unbiased estimator (for any noise distribution that obeys assumptions)
  Errors are zero mean, uncorrelated, and all have the same finite variance
If noise distribution is Gaussian, is the maximum likelihood estimator

## Slide 16: Persistent excitation
Classical question: what are sufficient conditions for our estimator to converge?

## Slide 17: Persistent excitation
Classical question: what are sufficient conditions for our estimator to converge?

## Slide 18: Persistent excitation
Classical question: what are sufficient conditions for our estimator to converge?

## Slide 19: Persistent excitation
 criterion such that if our sys id/adaptive control system operates forever, then we’ll have identified the system perfectly
Classical question: what are sufficient conditions for our estimator to converge?

## Slide 20: Performance questions
Practically, the system identification approach leads to several questions:
What if we have a data budget?
  How much data is required to learn the model?
  How can we quantify a “good” estimate?
  We care about controller performance, not model accuracy, so do we require an accurate model?
How should we design the inputs used for data collection?
  What if we’re learning while doing?
  What if an engineer can’t intervene to prevent system failure during data collection?
What if our system does not fall in the class of systems we are considering?

## Slide 21: Outline
Intro to learning settings
System ID
Adaptive control
MRAC: Model Reference Adaptive Control
MIAC: Model Identification Adaptive Control

## Slide 22: Adaptive control
Broadly, adaptive control aims to perform online adaptation of the policy to improve performance
This can be done via directly updating the policy or updating the model and re-optimizing or re-computing the controller
Most classical adaptive control work does not consider the optimal adaptive control problem; they focus on proving stability of the coupled controller + adaptive component + system dynamics

## Slide 23: Detour: Lyapunov theorem for global stability
Consider an autonomous system (e.g., ).
Equilibrium point: s.t.
1. for all ,
2. for all
3. as
If such a function exists, then equilibrium is globally asymptotically stable.

## Slide 24: Detour: stability analysis via Lyapunov
Mass/Spring/Damper
Consider the total energy of the system:

## Slide 25: Adaptive control approaches
Encompasses a large variety of techniques, including :
Model reference adaptive control (MRAC)
Model identification adaptive control (MIAC)

## Slide 26: Model reference adaptive control (MRAC)
A model reference adaptive controller is composed of four parts:
  A plant containing unknown parameters
  A reference model for compactly specifying the desired output
  A feedback control law containing adjustable parameters
  An adaptation mechanism for updating the adjustable parameters
Compared to reward functions, a reference model is an alternative way to specify how a system should behave
  The reference model provides the ideal plant response which the adaptation mechanism should seek in adjusting the parameters

## Slide 27: Example of MRAC control
Consider double integrator
Assume a human operator provides the positioning command to the control system
A reasonable way of specifying the ideal response of the controlled mass to the external command is to use the reference model
where the reference model output is the ideal output

## Slide 28: Example of MRAC control
If the mass is known exactly, one can achieve perfect tracking via
where is some chosen gain and is the tracking error
This control leads to exponentially convergent tracking dynamics

## Slide 29: Example of MRAC control
If the mass is not known exactly, we can use the control law
which contains the adjustable parameter
This control leads to the closed-loop dynamics
where:
  is a combined tracking error measure (the “sliding mode” variable), defined by
  the signal quantity is given by
  and the parameter estimation error is =

## Slide 30: Example of MRAC control
One way of adjusting the parameter is to use the (nonlinear) update law
where is called the adaptation gain
Stability and convergence can be analyzed via Lyapunov theory
Consider Lyapunov function candidate
Its derivative is
Thus , and hence and

## Slide 31: MRAC
An excellent reference for systematic MRAC design is: Jean-Jacques Slotine, Weiping Li, Applied Nonlinear Control, Chapter 8
If the reference signal is very simple, such as zero or a constant, it is possible for many vectors of parameters, besides the ideal parameter vector, to lead to tracking error convergence
However, if the reference signal is so complex that only the “true” parameter vector can lead to tracking convergence, then one shall have parameter convergence -> persistent excitation condition

## Slide 32: Model identification adaptive control
MIAC (also referred to as self-tuning) simply combines model estimation with a controller that uses the estimated model
Important distinction between certainty-equivalent and cautious approaches
  Certainty-equivalent: maintains point estimate of model and uses that model for policy selection/optimization. Can be suboptimal, risky.
  Cautious: Maintains measure of estimator uncertainty, incorporates the uncertainty into the controller. This is often overly robust because it does not account for future info gain!

## Slide 33: MRAC vs. MIAC
MRAC and MIAC arise from two different perspectives:
  parameters in MRAC are updated so as to minimize tracking error between the plant output and the reference model output
  parameters in MIAC are updated so as to minimize the data-fitting error
MIAC controllers are in general more flexible, as one can couple various controllers with various estimators
However, correctness of MIAC controllers is more difficult to guarantee, as if the signals are not rich, the estimated parameters may not be close to the “true” values, and stability and convergence may not be ensured
In contrast, for MRAC, stability and convergence are usually guaranteed regardless of the richness of the signals

## Slide 34: Next class
Intro to Imitation Learning (IL) and Reinforcement Learning (RL)