## Slide 1: AA203 Optimal and Learning-based Control
Intro to Imitation Learning (IL) and Reinforcement Learning (RL)

## Slide 2: Course overview
Open-loop
Indirect methods
Direct
methods
Closed-loop
DP
HJB / HJI
MPC
Adaptive
optimal control
Model-based RL
Model-free RL
Control
Optimal and learning control
Adaptive control
Feedback control
Imitation Learning

## Slide 3
Credits:
Credits:
Credits:
Gemini Robotics
Credits:

## Slide 4
[NVIDIA. Alpamayo-R1]

## Slide 5: Learning for control, in practice
12 DoF quadruped
Lidar
RGB front camera
Potentially hazardous terrain
…
How can we develop a reliable control algorithm?
Option 1
Deeply understand the problem
Design a solution
Success,
Failure
?
Option 2:
Imitation Learning
Option 3:
Reinforcement Learning
Upcoming weeks: Set it up as a learning problem
“Learn from demonstrations”
“Learn by trial and error”

## Slide 6: Outline
Primer on Supervised Learning
Imitation Learning
Reinforcement Learning
Key learning goals:
An overview of the fundamentals of IL and RL
Identify the distinctions and similarities between these paradigms
e.g., [dog, cat, …, mouse]

## Slide 7: Imitation Learning and Reinforcement Learning
Resources:
PoRA book Chapters 17-19, and references therein, and also:
  Sutton and Barto: “Reinforcement Learning: An Introduction”
Classes:
  Stanford CS 224R Deep Reinforcement Learning
  Berkeley CS 185/285 Deep Reinforcement Learning

## Slide 8: A primer on supervised learning (SL)
In SL, the task is to learn a mapping
from inputs
to outputs
e.g., [dog, cat, …, mouse]
Learning involves data in the form of input-output pairs , e.g., Maximum Likelihood Estimation

## Slide 9: Learning from a probabilistic standpoint
Let’s consider regression as an example
Learning through minimization of squared error

## Slide 10: Learning from a probabilistic standpoint
Let’s consider regression as an example
Learning through likelihood maximization:

## Slide 11: The basics of Imitation Learning
Imitation learning refers to a class of methods that enable skills to be transferred from an expert to a learner
In the context of robotics, the expert is typically a human operator or a pre-existing control policy and the learner is the robot that aims to mimic the expert’s behavior
Example:

## Slide 12: The basics of Imitation Learning
Assume access to a dataset of state-control pairs collected by an expert
At a high-level, approaches to IL belong to two main categories:
  Behavior Cloning “learn the policy used by expert”
  Inverse Reinforcement Learning “learn the objective optimized by the expert” (a.k.a. Inverse Optimal Control)
Behavior Cloning Inverse Reinforcement Learning

## Slide 13: Behavior Cloning (BC)
Main idea: Train policy via supervised learning
Skeleton of an IL algorithm:
Collect a dataset of “expert” demonstrations
Train policy to mimic expert:
e.g., MLE, cross-entropy, L2 / MSE, etc.

## Slide 14: A first (deep) imitation learning system
ALVINN: An Autonomous Land Vehicle In a Neural Network (1989)

## Slide 15: Is this guaranteed to work?
Spoiler: NO - Imitation learning is different from “plain” supervised learning
Supervised learning: learn a mapping from input data to output labels based on a dataset of input-output pairs
IL builds heavily on SL, however with some key differences:
  Even small prediction errors will compound over time
  The solution may have inherent structural properties, such as physical constraints or temporal dependencies, that are not present in standard supervised learning tasks
  In IL, the source domain may differ from the one at deployment (e.g., humanoid control by learning from videos of humans)
  Covariate shift, where the distribution of the expert’s data may differ from the distribution of the learner’s data
  Obtaining expert demonstrations may be expensive or time consuming
e.g., [dog, cat, …, mouse]

## Slide 16: Inverse Reinforcement Learning (IRL)
IRL takes an orthogonal approach to IL, by attempting to recover a reward function from a policy, or from demonstrations of a policy
Example: (BC vs IRL)
A warehouse robot must navigate from a starting point to a goal while avoiding obstacles.
Behavior Cloning:
Collect demonstration data, train a policy that imitates the demonstrations
Effective in familiar scenarios, however, it may struggle if the layout changes substantially
Inverse RL:
Collect the same demonstration data, infer the reward function (e.g., positive for moving closer to the goal, negative for moving close to obstacles)
The reward function encapsulates the underlying principles of the task

## Slide 17: Outline
Primer on Supervised Learning
Imitation Learning
Reinforcement Learning
Key learning goals:
An overview of the fundamentals of IL and RL
Identify the distinctions and similarities between these paradigms
e.g., [dog, cat, …, mouse]

## Slide 18: What is reinforcement learning?
Fundamentally:
A mathematical formalism for learning-based decision making
An approach for learning decision making and control from experience
take action
observe state
Most RL algorithms follow the same basic learning loop:

## Slide 19: What is reinforcement learning?
Elements of RL:
  Policy : a mapping from states to actions that defines the agent’s behavior
  Environment: the system the agent interacts with. Mathematically, we represent it as
  Reward : scalar measure of (immediate) success. Defines the goal of the agent
  Value function: measures performance in the long run. Defines how much the agent can expect to achieve in the future
  Model (optional): represents the agent’s understanding of the environment. Its goal is to mimic the behavior of the environment. Mathematically, we represent it as
take action
observe state

## Slide 20: Why reinforcement learning?
RL can discover new, unexpected solutions
“Move 37” in Lee Sedol AlphaGo match

## Slide 21: Why reinforcement learning?
RL algorithms are very effective at optimizing complex objectives, with virtually no assumptions on the reward structure
  This makes RL appealing for complex physical tasks

## Slide 22: Characteristics of reinforcement learning?
How does RL differ from other machine learning paradigms?
No supervision, only a reward signal
Feedback can be delayed, not instantaneous (i.e., credit assignment)
Data is not i.i.d., earlier decisions affect later interactions (tension between exploration and exploitation)

## Slide 23: Markov Decision Process
State:
Action:
Transition function / Dynamics:
Reward function:
Discount factor:
Typically represented as a tuple

## Slide 24: Some examples
State:
Action:
Dynamics
Reward function:
Chess
position of pieces
next move
given a move, defines the next configuration of the board (deterministic)
-1/+1 for lost/won game
State:
Action:
Dynamics
Reward function:
robot’s pose (e.g., foot positions, joint angles) and its position on the terrain
joint torque commands for each leg
the robot applies the chosen torque commands to its joints, deterministically resulting in the next pose and position based on the physics of the terrain
+10 forward step / -5 falling / 0 standing still
Quadruped

## Slide 25: Value functions
State-value function: “the expected total reward if we start in that state and act accordingly to a particular policy”
Action-state value function: “the expected total reward if we start in that state, take an action, and act accordingly to a particular policy”
Optimal state-value function:
Optimal action-state value function:
The majority of RL algorithms are defined via manipulations of these concepts

## Slide 26: A taxonomy of RL
RL Algorithms
Model-free
Model-based
Policy optimization
Value-based
Learn the model
use dynamics
do not use dynamics
Given the model
is known
directly maximize the RL objective
Estimate
policy implicitly defined via
or

## Slide 27: Why so many RL algorithms?
Different tradeoffs:
  Sample efficiency
  Stability & easy of use
Different assumptions:
  Stochastic or deterministic
  Continuous or discrete
  Episodic or infinite horizon
Different things are easy or hard in different settings:
  Easier to represent the policy?
  Easier to represent the model?
Adapted from CS 185/285

## Slide 28: Comparison: sample efficiency
Sample efficiency = how many samples do we need to get a good policy?
Crucial question: is the algorithm off policy?
  Off policy: able to improve the policy without generating new samples from the current policy
  On policy: each time the policy is changed, even a little bit, we need to generate new samples
Why even bother using less efficient algorithms? Wall-clock time is not the same as efficiency!
Adapted from CS 185/285

## Slide 29: Comparison: stability and ease of use
Does it converge?
And if it does, to what?
Does it always converge?
Supervised learning: almost always gradient descent
Reinforcement learning: often not gradient descent
  Q-learning: fixed point iteration
  Model-based RL: model estimator is not optimized for expected reward
Adapted from CS 185/285

## Slide 30: Some remarks
So far, it may be tempting to view IL and RL as “alternatives”
Today, IL and RL are widely used in scaffolded training pipelines, where both are essential for achieving the desired behavior, robustness, and overall performance.
[NVIDIA. Alpamayo-R1]
Imitation Learning:
Pros: Simplicity, Efficiency, No need for explicit reward signal
Cons: Dependence on demonstration quality, generalization, no exploration
Reinforcement Learning:
Pros: Autonomous discovery, long-term optimization in complex tasks, no labels
Cons: Training instability, sample inefficiency, reward function design

## Slide 31: Next class
Imitation Learning (IL)