## Slide 1: AA203 Optimal and Learning-based Control
Direct methods for optimal control, sequential convex programming (SCP)

## Slide 2: Roadmap
Open-loop
Indirect methods
Direct
methods
Closed-loop
DP
HJB / HJI
MPC
Adaptive
optimal control
Model-based RL
Model-free RL
Control
Optimal and learning control
Adaptive control
Feedback control

## Slide 3
Direct Methods:
Transcribe (OCP) into a nonlinear, constrained optimization problem
Solve the optimization problem via nonlinear programming
Optimal control problem
For simplicity:
We assume the terminal cost is equal to 0
We assume
Indirect Methods:
Apply necessary conditions for optimality to (OCP)
Solve a two-point boundary value problem
,
(OCP)
,

## Slide 4: Direct methods
Resources:
Notes Chapter 5 and references therein, and also:
  Rao A. V., “A survey of numerical methods for optimal control,” 2009.
  Kelly, M., “An Introduction to Trajectory Optimization,” 2017.

## Slide 5: Transcription methods
Optimization: what are the decision variables?
State and control parameterization methods
  “Collocation”/“simultaneous”
Control parameterization methods
  “Shooting”

## Slide 6: Transcription into nonlinear programming (state and control parametrization method)
Forward Euler time discretization:
Select a discretization for the interval and, for every , define and
By denoting , (OCP) is transcribed into a nonlinear, constrained optimization problem
(NLOP)
,
(OCP)
,

## Slide 7: Illustrative example: Zermelo’s Problem
Current flow
t [0, ]
,
, t [0, ]
, t [0, ]
(OCP)

## Slide 8: Example: Zermelo’s Problem (state and control parametrization method)
Transcribe optimal control problem into a non-linear program, and solve it via fmincon (MATLAB), scipy.optimize.minimize (python), etc.
,
,
(NLOP)
t [0, ]
,
, t [0, ]
, t [0, ]
(OCP)

## Slide 9: Results
(effectively, no control constraint)

## Slide 10: Transcription into nonlinear programming (control parametrization method)
Time and control discretization:
,
(OCP)
,
(NLOP-C)
where each is recursively computed via
Select a discretization for the interval and, for every , define
By denoting , (OCP) is transcribed into a nonlinear, constrained optimization problem

## Slide 11: Example: Zermelo’s Problem (control parametrization method)
Transcribe optimal control problem into a non-linear program, and solve it via fmincon (MATLAB), scipy.optimize.minimize (python), etc.
t [0, ]
,
, t [0, ]
, t [0, ]
(OCP)
,
(NLOP-C)
where, recursively:

## Slide 12: Results
(effectively, no control constraint)

## Slide 13: Example: Zermelo’s Problem
,
,
(NLOP)
t [0, ]
,
, t [0, ]
, t [0, ]
(OCP)
,
(NLOP-C)
where, recursively:
Direct Transcription
Direct Shooting

## Slide 14: Transcription methods: extensions
Multiple shooting
  Hybrid of simultaneous / (single) shooting methods
Alternative trajectory parameterizations
  Euler integration (above): piecewise linear effective state trajectory (C0), zero-order hold control trajectory
  Hermite-Simpson collocation (see Notes §5.2.1): piecewise cubic effective state trajectory (C1), first-order hold control trajectory
    Dynamics constraint is enforced at “collocation points”, exact form is derived by implicit integration
  Pseudospectral methods: global polynomial basis functions (instead of piecewise polynomials)
  Shooting methods: higher-order integration schemes (e.g., RK4)
    Dynamics constraint is enforced by explicit integration

## Slide 15: Sequential Convex Programming
,
,
,
The sources of nonconvexities are the dynamics and (possibly) the cost. Idea: linearize (and convexify) them around nominal trajectories!
Assume that is convex. Let be a nominal tuple of trajectory and control. does not need to be feasible!
Linearize around :
Solve the new problem for

## Slide 16: Sequential Convex Programming
The sources of nonconvexities are the dynamics and (possibly) the cost. Idea: linearize (and convexify) them around nominal trajectories!
,
,
,
Iterate this procedure until convergence is achieved: linearize around the solution at iteration :
  and solve the problem for

## Slide 17: Sequential Convex Programming
,
,
,
Discretize and solve a convex problem at each iteration
Select a discretization for the interval and, for every , define and
By denoting , is transcribed into the following convex optimization problem
,

## Slide 18: Sequential Convex Programming
,
,
,
Linearize around the solution
Define the continuous time problem
Discretize in time and define the convex optimization problem
SCP Methodology: at each iteration
Solve via convex programming for a discretized version of
,

## Slide 19: Sequential Convex Programming
For more info: D. Malyuta et al., "Convex Optimization for Trajectory Generation: A Tutorial on Generating Dynamically Feasible Trajectories Reliably and Efficiently," in IEEE Control Systems Magazine, vol. 42, no. 5, pp. 40-113, Oct. 2022.

## Slide 20: Direct Methods in Practice
“As you begin to play with these algorithms on your own problems, you might feel like you're on an emotional roller-coaster.” – Russ Tedrake
Better initial guess trajectories (“warm-starting” the optimization, as seen in zermelo_simultaneous)
Cost function/constraint tuning (as seen in zermelo_scp)
  Penalty methods; augmented Lagrangian-based solvers

## Slide 21: To wrap up…
Local vs Global solution
Less vs more compute
High- vs low-dimensional system

## Slide 22: Next time
Dynamic programming
Discrete LQR